## Slide 1: Hessian based Mesh adaptivity
Lohith

## Slide 2: What is HBA
For normal adaptation we find the error between the exact value and the approximated value in some norm.
If this error involves the second order derivative of the exact solution then it is called hessian based adaptivity.
Eg:
U-exact solution, omega is domain, h-mesh size, uh is the finite element approximation, C is a positive value independent of h and u but depends on the aspect ration of finite element.

## Slide 3: Why Hessian based adaptivity?[1]
It is independent of the specific problem being solved.
It provides stretched meshes to capture boundary and internal layers
The idea of governing the mesh generation process by an auxiliary non Euclidean metric, which does not obtuse angles, results in that the meshes can indeed be built automatically.
The ability to adapt the size, shape, and orientation of mesh elements according to certain quantities of interest can signiﬁcantly improve the accuracy of the solution and enhance the computational eﬃciency.

## Slide 4: How is it done? Recovery methods:
QLS: Quadratic least squares fitting.
DLF: Double Linear least squares fitting.
LLS: Linear least squares fitting.
WF: variational method/ Weak Formulation.

## Slide 5: Recovery Methods:
Quadratic Least Squares fitting:
  involves the ﬁtting of a quadratic polynomial to given function nodal values and the subsequent diﬀerentiation.
  The original purpose of QLS is the gradient recovery. However, the method is easily adopted for the needs of the Hessian recovery by simply diﬀerentiating the obtained ﬁtting polynomial twice.
  For a given node, at least ﬁve nodes from its direct neighbourhood (patch) are selected. The original function is then approximated on the selected patch by ﬁtting a polynomial of degree two to the function values at the selected nodes in the least square sense.

## Slide 6: Recovery Methods:
Node N0(x0,y0), patch is rep as Ni(xi,yi) i=1,2,..n for n>=5.
Uh-approximated function.
Polynomial p2: p2 (x,y;N0)=a1+a2x+a3y+a4xy+a5x2+a6y2
Coeff vector a=(a1,a2,a3,a4,a5,a6)T is computed by solving system of equations ATAa=ATUh.

## Slide 7: Recovery Methods:
Double Linear Least squares fitting:
  Double linear least squares ﬁtting computes the derivatives by smoothing the linear approximation of a given function before computing derivatives.
  The process is similar to the smoothing process described for the quadratic least squares ﬁtting except for the order of the ﬁtting polynomial. Here, a linear regression is applied.
  Again for node N0(x0,y0), let n be the number of direct mesh neighbours Ni(xi,yi) i=1,2,..n for n>=5.
  The local linear approximation p1(x,y;N0) over patch of N0 is given by,
p1(x,y;N0)=a1+a2x+a3y

## Slide 8: Recovery Methods:
Rank of A.
The recovered gradient is given by,
Second-order derivatives are obtained by subsequent application of the described algorithm to the calculated ﬁrst order derivatives.

## Slide 9: Recovery methods:
Linear Least Squares fitting:
  Same as DLF except for the reverse order of the smoothing and derivation steps.
  First-order derivatives of a given piecewise linear function are computed at the element centres and smoothed afterwards by means of linear least squares ﬁtting.
  Second-order derivatives are computed in the same way from the nodal approximation of the ﬁrst-order derivatives.

## Slide 10: Recovery Methods:
Variational Method using Weak Formulation:
  This approach recovers the Hessian, which does not exists in the classical sense for piecewise linear functions, by means of a variational formulation.
  The nodal approximation to the second-order derivative of u at N(xi,yi) is defined as,
  In the same way uxy, uyy are approximated.
  ⏀i are piecewise linear basis functions.
  This method is quite simple, fast and widely used in practice

## Slide 12: Numerical Comparison:
We will consider the lagrangian interpolation.
The Hessian is recovered from the exact nodal values of a given test function and compared with the exact analytical Hessian.
We will also compare the behaviour in relation to the mesh type.
QLS:
  The QLS recovery is exact for quadratic functions independent of the mesh type.
  QLS hessian recovery on diff. mesh types:
  L2 recovery error vs # of mesh elements.
  uQ(x,y)=x2+y2

## Slide 13
  Uniform Meshes:
  L2-Norm of the relative recovery error vs the number of elements on uniform meshes is studied. Results obtained for different test functions can be summarised as shown.
  Quadratic Function:
  LLS and WF methods both provide exact hessian recovery with error smaller than 10-8.
  DLF is inexact on uniform meshes for quadratic function. Fig: a.

## Slide 14
  Gaussian Function:
  Plot b shows recovery of Gaussian function, which is dominated by error in domain interior, since the test function is zero on boundary.
  All four methods show similar convergence results( n-1 ≡h2), but DLF has a slightly larger error.

## Slide 15
Boundary Layer:
Figure below presents relative recovery errors of boundary layer functions.
The recovery error is dominated by the error near boundaries.
Again QLS, LLS, WF provide similar results, but experience accuracy losses.
DLF is less accurate with error O(n-1/4)≈O(h1/2).

## Slide 16
Anisotropic Function:
Figure presents the results,
The convergence rates for QLS, LLS and WF are about n-3/4 ≈h3/2
DLF once again is not as good as other methods, even less accurate on finer meshes.

## Slide 18: References
On Hessian Recovery and Anisotropic Adaptivity.